## Slide 1: Switched Nonlinear Systems: Stability Analysis via Average Dwell Time and Average Activation Time Switching
Shenyu Liu
School of Automation, Beijing Institute of Technology

## Slide 2: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 3: Related work
[A] Liu, S., Russo, A., Liberzon, D. and Cavallo A. (2021). On Integral Input-to-State Stability of Time Dependent Switched Systems with Dwell Time Switching. IEEE Transactions on Automatic Control vol. 67, issue 11, 5841–5855.
[B] Liu, S., Tanwani, A. and Liberzon, D. (2021). ISS and Integral-ISS of Switched Systems with Nonlinear Supply Functions. Mathematics of Control, Signals, and Systems, vol. 34, 297–327.
[C] Liu, S., Russo, A. (2022). Further characterizations of integral input-to-state stability for hybrid systems. Provisionally accepted by Automatica.
[D] Eising, J., Liu, S., Martinez, S. and Cortes, J. (2022). Using Data Informativity for Online Stabilization of Unknown Switched Linear Systems. In proceedings of the 61st IEEE Conference on Decision and Control, 8–13.
[E] Liu, S. (2022). Characterizations and Stability Criteria for the 2-Mode Markovian Switched Nonlinear Systems. Conditionally accepted by IEEE Transactions on Automatic Control.
[F] Liu, S. Wen, P. (2023). Non-conservative Stability Criteria for Semi-Markovian Impulsive Switched Systems. Submitted to SIAM Journal of Control and Optimization

## Slide 4: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 5: What is a switched system?
Switched systems comprise a family of dynamical systems orchestrated by a piece-wise constant switching signal
It provides a framework for modeling systems with transitions of dynamics and state jumps
Daily life examples: Air conditioner, refrigerator, auto gearbox, the smart traffic light systems, etc.
Control systems examples:
  Supervision control of systems with large uncertainties;
  Sampled-data control of cyber-physical systems
  Event-triggered control
  Quantized control

## Slide 6: Why switching?
The model of switched systems capture rich dynamical behavior
Continuous-time systems not stabilizable via continuous state-feedback can be stabilized via switched control
Non-robust stability becomes robust
Switched feedback control improves performance
…

## Slide 7: Definition of switched systems
，system state trajectory
，input signal or disturbance
，switching signal
Assumptions on the switching signals
  Càdlàg (Right-continuous with left limits exist)
  Non-Zeno (finite number of discontinuities over finite time interval)
Dynamics of subsystems：
1
2
3

## Slide 8: Feature of stability of switched system
Stability is a key property studied for control systems
Consider the case of an autonomous or unforced system，
Consider Global asymptotic stability (GAS)
For a switched system to be GAS under arbitrary switching signal, it is necessary to require all subsystems to be GAS.
However, this condition is not sufficient.

## Slide 9: Conceptual example
Existence of a divergent solution of a switched system with both GAS subsystems.

## Slide 10: How to avoid instability?
Switch at the right moment
  Need to monitor at all time
  Event-triggered
Switch at low frequency
  No need to monitor
  Restrict dwell-time (DT), or
  Restrict average dwell-time (ADT),
Let one subsystem be dominant
  No need to monitor
  Restrict activation time (AT), or
  Restrict average activation time (AAT),
Impose ADT-AAT mixed conditions
State-dependent
Time-dependent

## Slide 11: Control system example:
De Persis & Tesi. TAC, 2015.
A networked, sample-data cyber-physical system, subjected to denial-of-service (DoS) attack.
DoS attack in the communication network is modeled by its frequency (~DT or ADT), and its duty ratio (~AT or AAT).

## Slide 12: Recap of stability definitions
An autonomous switched system is globally asymptotically stable (GAS) uniformly over if there exist such that
for all and .
A switched system with inputs is input-to-state stable (ISS) uniformly over if there exist , such that
for all and .
A switched system with inputs is integral input-to-state stable (iISS) uniformly over if there exist such that
for all and .

## Slide 13: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 14: ADT condition
Assume autonomous
Assume all GAS subsystems
Assume the existence of smooth Lyapunov functions ，constants ，such that for all ，it holds that
Linear supply functions

## Slide 15
,
,
,
.
Total number of switches over time interval

## Slide 16
If there exists ，such that
then it can be computed that
Hence, the system is GAS.
ADT condition：
On average, there is at most one switch per unit of time.
Sufficient condition:

## Slide 17: AAT condition
Assume autonomous
Assume 2 subsystems, one GAS and one unstable.
Assume the existence of a smooth Lyapunov function ，constants ，such that for all ，it holds that

## Slide 18
,
,
.
Total activation time of subsystem 2 over time interval

## Slide 19
If there exists ，such that
then it can be computed that
Hence, the system is GAS.
AAT condition：
On average, activation of a (some) mode takes at most a ratio of of the total time.
Sufficient condition:

## Slide 20: ADT-AAT mixed condition
If the switching signal satisfies both ADT and AAT conditions with parameters satisfying
then the switched system is GAS.
Equivalently,
Müller & Liberzon. Automatica, 2012

## Slide 21: Remarks
Previous inequalities hold with sufficiently small and sufficiently large .
Similar analysis carries through for showing ISS switched systems. Same conditions are obtained for ADT and AAT [Vu et al, 2007], [Müller & Liberzon, 2012].
The key ingredient is the assumption of linear supply functions. This does not hold for iISS.
Also for switched nonlinear systems, the supply functions are likely nonlinear as well and can not be majorized to be linear.

## Slide 22: Bilinear system with Hurwitz is iISS
Consider a bilinear system with single input
To show iISS, one can pick Lyapunov function [Chaillet et al, 2014]
This gives
This function is only

## Slide 23: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 24: Non-trivial examples
Switched systems which are not GAS under ADT switching signals, no matter how slowly it switches.
or
[A],
Della Rossa & Tanwani. SCL 2022

## Slide 25: Motivation
There are examples of switched systems with nonlinear supply functions, which are not GAS, ISS or iISS uniformly over any class of ADT switching signals
Questions:
  What weaker stability properties do such systems have?
  [A], [C]
  Are there switched systems with nonlinear supply functions that are GAS, ISS or iISS uniformly over ADT switching signals? What are the sufficient conditions?
  [B]
  Does there exist a more restrictive class of switching signals, uniformly over which the aforementioned systems with nonlinear supply functions are GAS, ISS or iISS?
  Liu, Tanwani, Liberzon, in preparation

## Slide 26: Weaker stability properties
The switched system is quasi-iISS (qiISS) under slow switching if for all , there exist a dwell time and functions , such that
for all .
The switched system is integral-input-to-state practically stable (iISpS) under slow switching if for each , there exist a dwell time and functions , such that
for all .

## Slide 27: Weaker stability properties
The work [A] proposes DT conditions for a switched nonlinear system to be qiISS or iISpS.
Using these conditions, the aforementioned examples, after adding disturbance, are proven qiISS and iISpS, respectively.
We also show that, a switched system is iISS if and only if it is both qiISS and iISpS.
Similar results are also carried out for ISS [C] but done in the hybrid system framework.

## Slide 28: Lyapunov characterization via nonlinear supply functions
Assume the existence of smooth Lyapunov functions functions such that for all it holds that
The subsystems with index are iISS.
If then those subsystems are ISS.
A mild assumption: is one-sided globally Lipschitz.

## Slide 29: Sufficient conditions for ISS and iISS
Define
Stability result: The switched system is iISS uniformly over all switching signals satisfying ADT-AAT conditions, with parameters satisfying
Moreover, if , then the switched system is ISS uniformly over the same class of switching signals.
[B]

## Slide 30: Sketch of the proof
The proof is evolved in the framework of hybrid systems
  Construct hybrid timers for dealing with ADT and AAT conditions
  Define a hybrid Lyapunov function
  where
  Show (1) a sandwich condition, (2) dissipative along flow maps (3) dissipative along jump maps for the hybrid Lyapunov function .

## Slide 31: Observations
For switched system with linear supply functions, the condition becomes
same as [Müller & Liberzon, 2012].
Using this theorem, switched bilinear systems is shown iISS under slow switching.
Autonomous linear systems, linear systems with linear inputs, bilinear systems are fundamentally alike:
If a condition on ADT, AAT guarantees a GAS autonomous switched linear system, then it also guarantees ISS switched linear system with linear inputs and iISS switched bilinear system with the same matrices.

## Slide 32: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 33: Why data-driven
Control a system without knowing the exact system parameters
For a linear discrete-time system
one does not need to collect as many data as for identification of , in order to design a stabilizing feedback law
Data informativity [van Waarde et al, TAC 2020]
Space of all systems
Systems compatible with the collected data

## Slide 34: Data-driven online stabilization
are all unknown.
is also unknown (but satisfies some DT/ADT conditions).
Design a control law to stabilize the switched system.

## Slide 35: Existing algorithm
At each time instant , the algorithm solves a semidefinite program (SDP) based on data collected over a finite window, and hence find a state feedback law .
If there is a switch in the window, then the computed gain does not help stabilizing the system.
Window size needs to be large. Past data is discarded; the algorithm updates as if it has no previous knowledge about the system at all.
In order to mitigate such problems, the switching needs to be very slow so that most of the time, the system dwells in a single mode over the finite window.
SDP at each time instant makes the algorithm inefficient.
Rotulo et al, Automatica, 2022

## Slide 36: Our algorithm
Initialization phase: collect a minor amount of data for finding a for each mode .
Mode detection phase: use data compatibility condition for detecting the current mode.
Stabilizing phase: apply , where is the detected mode from mode detection phase.
Initialization
Mode detection
Stabilization
Mode detected?
Triggering condition met?

## Slide 37: Advantages of our approach
Mode detection scheme
Triggering condition (noiseless)

## Slide 38: Stability analysis
Each stabilizing phase is a stable subsystem
Each mode detection phase is an unstable subsystem
Stability can be analyzed via ADT-AAT conditions
The results show that our approach allows switching signals with much faster switching.
[C]

## Slide 39
A numerical example with 5 states, 3 inputs, and 5 modes

## Slide 40: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 41: Stochastic vs deterministic
Unlike deterministic switching signals, a stochastic switching signal can have random switches.
Frequency of switches and activation time of modes are also random.
ADT, AAT conditions becomes unsuitable.
However, expectations of dwell time and activation time still make sense.
ADT, AAT conditions can be imposed on these expectations.

## Slide 42: Markovian/semi-Markovian switched systems
Dynamics is the same as deterministic switched systems
Switching signals are generated by Markov/semi-Markov processes:
  , initial probability vector
  , mode-transition probability matrix
  , sojourn time distribution functions
If all are exponential distributions, then it reduces to Markov process.

## Slide 43: Stochastic stability definitions
Almost sure global asymptotic stability (GAS a.s.):
Asymptotic -th moment stability: there exists such that
When or , they are also known as asymptotic mean stability or asymptotic mean-square stability.

## Slide 44: GAS a.s. via ADT and AAT
Compute expected dwell time and activation time:
  Let be the left Perron vector of . This eigenvector tells the steady state of the discrete-time Markov process with transition matrix .
  Expected dwell time of subsystem :
  Expected switching period:
  Expected activation time of subsystem :
Stability result: if it holds that
then the switched system is GAS a.s.
The proof uses ergodicity theory.
[Wu et al. TAC 2018]

## Slide 45: Is GAS a.s. a good measure?
Consider a 2-mode, 1-dimensional, switched linear system

## Slide 46: Is GAS a.s. a good measure?
GAS a.s. is an asymptotic property, not satisfactory in the prediction of when is finite.
It cannot reflect the statistical behavior of .
GAS a.s. is different to asymptotic moment stability, and asymptotic moment stability differs with respect to different degrees of moment.

## Slide 47: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 48: Assumptions on sojourn time distributions
For all , is continuous and -times piece-wise continuously differentiable.
High-order “derivative” of : and for each
is the “derivative” of , modulo the non-smoothness and discontinuities.
Define

## Slide 49: Assumptions on sojourn time distributions
Assumption 1: For each , there exist such that
Assumption 2: The set
is finite. Moreover, for all , .
These assumptions hold for standard distributions; e.g., exponential, uniform, trigonometric, Gamma (with integer shape parameter) distributions, etc.

## Slide 51: Lyapunov functions assumption
Assumption 3: There exist smooth functions , functions and parameters , such that for all it holds that

## Slide 52: Sufficient condition for asymptotic moment stability
Consider a semi-Markovian switched system with modes, where its switching signal . Suppose all Assumptions 1,2,3 hold. Then it holds that
where is the single output of the -dimensional linear time-delay system
[F]

## Slide 54: Remarks
This theorem establishes a close relationship between the asymptotic moment stability of a semi-Markovian switched system and GAS of an auxiliary linear time-delay system.
The semi-Markovian switched system is asymptotic -th moment stable if the auxiliary linear time-delay system is GAS, and there exists such that
The result is tight, in the sense that if all the inequalities in the Lyapunov functions assumption are replaced by equality, then the inequality in the estimation of moment expectation can also be replaced by equality.

## Slide 55: Remarks
The tightness comes from the novel derivation, which involves formulating a general multi-mode renewal equation, where no relaxations are introduced.
In the case of Markovian switched system (so that the sojourn time distributions are all exponential, ), the auxiliary system has no delay and is simply LTI.
Thus, it is sufficient to check whether the matrix is Hurwitz for showing asymptotic moment stability.

## Slide 56: Special case: 2-mode Markovian switched system
Necessary and sufficient condition for to be Hurwitz:
The second equation implies , which, after substituting becomes
[D]

## Slide 57: Intuitive conclusion
The sufficient conditions for asymptotic moment stability are stronger than those for GAS a.s.
When are small (i.e., decay/growth rates are relatively much slower than expected mode-changing rates), the two sets of assumptions are close.

## Slide 58: Numerical example

## Slide 59: On stochastic stability properties
Our estimations for expectations of state-norm and state-norm-square are non-conservative.
Even the expected sojourn time and mode transition probability are known, asymptotical moment stability is still inconclusive.
Unlike GAS a.s., ADT and AAT conditions are insufficient for determining asymptotic moment stability.

## Slide 60: Outline
Switched system overview
Deterministic stability
  Stability/stabilization via ADT/AAT switching
  General ISS/iISS switching signals for switched systems with nonlinear supply functions
  Application study: data-driven approach for online stabilization of unknown switched linear systems
Stochastic stability
  GAS a.s. via ADT/AAT conditions
  Asymptotic moment stability via studying auxiliary linear time-delay system
Conclusion and future work

## Slide 61: Conclusion and future work
This talk demonstrates how deterministic and stochastic stability properties of switched nonlinear systems are related to the ADT and AAT conditions imposed on the switching signal.
Compared with deterministic stability properties, stochastic stability properties of switched nonlinear systems are less studied.
  Closer investigation of the auxiliary linear time-delay system
  Extension from autonomous systems to systems with inputs: stochastic ISS properties
  Extension to nonlinear supply functions
  Application: what real switched systems are semi-Markovian?

## Slide 62: Q&A